OBD GPS Car Positioning Communication Terminal

（GPS+GSM+SMS/GPRS）

Installation instruction

（Version V2.0）

Please read carefully the installation guide before using so that to get the correct installation and use operation quickly. If product appearance and color have change, please subject to the real goods!

Contents

1．Product accessories

2．Product function

3．Install instruction

4．Instructions

5．Fault resolution

6．Warranty

1．Product accessories

1.1 : Main engine

1.2 ：Instruction

2. Product function

2.1 GSM850 / 900/1800 / 1900MHZ quad-band systems worldwide;

2.2 Wide operating input voltage range: 8-50VDC

2.3 GPS / LBS real-time positioning, mobile tracking and wechat tracking;

2.4 Supports SMS text query location information;

2.5 Built-in vibration sensor, and achieve intelligent vehicle anti-theft;

2.6 Platform supports up to the 180 days historical trajectory and line inquiry;

2.7 Platform support the electronic fence, out of area alarm;

2.8 Platform Support departing from the planning line alarm;

2.9 Platform Support overspeed alarm;

2.10 Platform supports serious collision warning (optional);

2.11 Platform supports rollover warning (optional);

2.12 Platform supports the report output;

2.13 Supports under WEB released anti and disarm;

3. Install instruction
3.1 Preparation before installation:
-3.1.1 open the box, check the device type whether is correct and accessories whether are complete, otherwise please contact your dealer;
-3.1.2 SIM card selection, the terminal need to insert a GSM SIM card, GSM card is universal for the local GSM network. (GSM networks is universal)
-3.1.3 SIM card installation, open the terminal device, set off the metal SIM card slot, down the SIM card chip into the slot, and then covered with a metal slot cover.

Note: ⑴ before installing or removing the SIM card, please firstly switch off the power of terminal which on the side;
⑵ terminal SIM card need to open GPRS function;
⑶ terminal SIM card need to open the Caller ID function (Depending on the customers needing function to choose to open or not open);
⑷ If your SIM card asks SIM PIN when is turned, please consult your phone's user manual and disabled the SIM PIN function;
⑸ Make sure that the SIM card terminal charges.

3.2 Installation
Directly into the OBD interface, not need any cable, simple and convenient. This image just for your reference about installation.

3.5 Step of product usage: Install → Power → Setting → Register
Installation: when install, the GPS antenna should be facing toward the sky, the above of installation mounting location must be no material (such as metal, Window Film) that will absorption of electromagnetic waves sheltered place.
Power: in correct direction to install the SIM card, according to the terminal diagram picture to install well line, and then slide the power switch.
Setting: must be done, or can not carry out other operations, use the car owner mobile phone to send text messages for terminal SIM card and set the owner number and a specific number.
Registration: registration method based on dealer platforms, registration method, because it is different, please consult your dealer.

3.6 Indicators

3.6.1 Yellow light-GSM indicator

| Light status | Mean |
| --- | --- |
| Flash one time within 2 seconds | GSM initialization |
| Steady light | GPRS normal communications/online |
| Not light | GSM sleeping |

3.6.2 Blue light-GPS indicator

| Light status | Mean |
| --- | --- |
| Flash one time within 2 seconds | GPS signal search |
| Steady light | GPS targeted |
| Not light | GPS sleeping |

4. Instructions

Note: GPS vehicle positioning terminal set communication parameters via SMS, the owner use their phone number send an SMS code to the GPS vehicle positioning terminal communication SIM card number, separated by a comma sign, the following function parameters instruction format comma in English input state format.

4.1 Owner password settings

Owner password number just can bind a number, the last binding owner number is effective

The owner default password: 123456

Set owner instruction number: admin123456 13712345678 and reply: admin ok

Modify the owner password command: password123456 666888 (666888 is new password) and reply: password ok

4.2 SOS specific number settings

Specific number is alarm number, you can send an SMS about increase specific number instruction to add a number, and you also can add two SOS specific number, 101 is the default owner number, 102 is the first SOS specific number, 103 is the second SOS specific number. In the alarm state, the terminal will send location or help information to specific number (information is according to whether you need to set), and will cycle call until the dial up. Before setting specific numbers, all numbers can be set and query. After setting a specific number, without password instruction can only set by associated specific number.

4.2.1 increase a specific number:

Instruction format: 102 # number #

Example: 102 # 13712345678 #

Reply message: OK

4.2.2 delete a specific number:

Instruction format:

D101 #

D102 #

D103 #

Example: D101 # means to delete the first number.

Reply message: OK

4.2.3 Query a specific number:

Instruction format: C10 #

Example: C10 #

Reply information: 101 # 13712345678

102 # 13712345688

103 # 13712345698

4.3 vibration alarm settings

4.3.1 Open vibration alarm messages: 125 # (default)

Reply message: OK

4.3.2 off the vibration alarm messages: 126 #

Reply message: OK

4.3.3 open vibrate phone alarm: 122 #

Reply message: OK

4.3.4 off the vibration alert: 121 # (default)

Reply message: OK

4.3.5 set the vibration alarm SMS command durable to 1-15 seconds.

Instruction: vibtime123456, n    Reply: vibtime set ok

n (0 ~ 15), 0 to cancel vibration alarm, default value is three seconds, mean 3 seconds vibration alarm

4.9 SMS text query location information
4.9.1 When query terminal device location information, you can write location query text messages and then sent to the SIM card on the terminal device, the terminal will reply the last position information.
SMS instruction: 123
4.9.2 owner card number call to equipment card number and send location information, ring twice to hang up.
4.9.3 Google Link SMS instruction: g1234

4.10 speed alarm settings
Overspeed alarm SMS speed limit: speed123456 080  set the speed limit of 80 km / h
4.10.1 Close speeding SMS notifications: speed123456 000 (default) Reply: speed ok
4.10.2 Open speeding SMS notifications: speed123456 080 Reply: speed ok

4.11 Displacement alarm settings
Displacement alarm setting instruction: move123456 300 (default)  Unit: m  Reply: move ok

4.12 fortification and cancel SMS settings
SMS fortification: SF Reply: SF OK
SMS fortification cancel: CF Reply: CF OK

4.14 GPS restart

SMS commands: CQGPS

4.15 Restore Factory Settings:

SMS commands: FORMAT

4.16 device reboot

SMS commands: CQ

4.17 Query device information

SMS commands: CXZT

4.18 APN settings:

Setting APN instruction format: apn123456 cmnet

Reply: apn ok

Setting APN corresponding user name instruction format: apnuser123456 user

Reply: apnuser ok

Setting APN corresponding password format: apnpasswd123456 password

Reply: apnpasswd ok

4.19 Setting the server IP and port:

SMS commands: IP + space + IP address + space + port number

Example: IP 219.143.106.193 8500 Reply: set IP OK

4.20 Application Platform (the dealer platforms are different, please consult your dealer internet site)

4.20.1 real-time monitoring, network / phone tracking

GPS + LBS dual-mode positioning, GPS positioning accuracy of 2 meters, when have GPS signal, GPS positioning, if no GPS signal, use LBS location station positioning. Dual-mode automatic switching let your GPS vehicle positioning terminal communication always online, and make sure you monitoring 365 days × 24 hours always online.

4.20.1 phone real-time monitoring: mobile internet domain login

4.20.2 Real-time monitoring platform: computer internet domain login

Example: Chinese www.aika168.com English: http: //3.tkstargps.net

4.20.2 track playback

Landing platform, click on the historical track playback function

4.20.3 report statistics

Logistics companies through this software to set the goods departure time, route point, line alarm, warning area, heavy hit the alarm, rollover warning, driving speed, etc. we will comprehensively analyze the goods in transit situation and issue reports.

Landing platform, please into statistics reports.

五．Troubleshootin

5.1 The terminal first time installed cannot connect to the back-end server, Background display is not online , please check the terminal installation.

5.1.1 Check the mains connection is correct, careful not received the vehicle interior control line.

5.1.2 Check SIM card is installed correctly, refer to the installation instructions.

5.1.3 Check The power switch is turned on.

5.1.4 Check the LED status, please refer to the indicators instruction

5.1.5 Check the GPS locate，if not locate please go to the open air place for the first time locate.

5.2 Terminal in the background display offline

First check the equipment three lights is normal, in the absence of conditions to observe the situation, you can check the status of the SIM card, follow these steps:

5.2.1 Call the SIM card number of the device, check if you can hear the phone connected  voice.

5.2.2 whether the vehicle is in the basement does not cover the GSM network signal.

5.2.3 Observation offline region, individual or all QQ offline, to determine whether the operators network problems.

5.2.4 whether  the SIM card is delinquent.

5.2.5 whether GPRS service is canceled (offline because last day of month  ).

5.2.6 Check parameter settings, view GPRS transmission time interval is correct.

5.3  If the terminal GPS function has been activated, but for a long time does not locate, check the terminal installation location meets the requirements, please refer to the installation instructions.

5.4  When the GPS signal reception environment is poor(surrounding tall buildings block the GPS signal), please drive to the open air for locate, generally need 1-2 minutes